## Slide 1
Case Example - Regression
Developing a Model for Process Improvement Using Multiple Regression Technique
Input
Output
Process Variables (x’s)
Noise Variables (z’s)
Input Variables (x’s)
Output
Measures
(y’s)
Effectiveness
(QPD)
Efficiency (η)
Fig-1: A general process model

## Slide 2
Case Example - Regression
The problem:
In a typical fiber plant viscose staple fiber or yarn are produced from wood pulp and spinning is one of the critical stages of operation.
The viscose pulp is forced through a spinneret, a device resembling a shower head with many small holes. Each hole produces a fine filament of viscose. As the viscose exits the spinneret, it comes in contact with chemical solution called spin bath. The result is the formation of fine filaments of cellulose, or rayon.
Evaporation being a critical process for maintaining the spin bath parameters. The main purpose of multi stage flash evaporator (MSFE) is to remove the excess water in spin bath solution, which is generated during the spinning process, to convert the spin bath solution to a concentrated spin bath solution.
The efficiency of MSFE is measured as M3 of water evaporated per ton of steam.

## Slide 3
Case Example - Regression
The problem:
In the fiber plant under study, around 4.5 ton/hr of steam is consumed for each MSFE.
Excess steam consumption increases the variable cost and the cost of production.
At present, the steam efficiency of MSFE is estimated to be 3.28 M3 of water evaporated per ton of steam. The target is to improve it up to 3.40 M3 .
It is expected to save 3317 ton of steam per annum amounting to a monetary saving of Rs 15.9 lac per annum for an average fiber production of 60 ton per day/MSFE.

## Slide 4
Case Example - Regression
The process:
Fig-2: Schematic Diagram of MSFE

## Slide 5
Case Example - Regression
The process parameters affecting the MSFE efficiency have been identified through technical discussion. These are:
Spin Bath Circulation Pressure ( X1 )
Cooling Tower Pressure ( X2 )
Cooling Tower Temp ( X3 )
V-9 temperature (X4 )
A-1 temperature ( X5 )
H-1 temperature ( X6 )
De Super Heater (DSH) temperature ( X7 )
Steam flow ( X8 )
Heater Pressure(X9)
The output variable (Y) is MSFE efficiency

## Slide 6
Case Example - Regression
Y = - 5.09 + 0.823 X1 + 0.247 X2 - 0.0137 X3 + 0.0375 X4 + 0.00248 X5 + 0.0605 X6 + 0.00368 X7 - 0.000492 X8 + 0.178 X9
withR2 value of 0.69 and R2adj value of 0.673.
The predictive model :
Predictor | Coefficient | SE Coefficient | t | P | VIF
Constant | -5.087 | 1.112 | -4.57 | 0.000 | 
X1 | 0.823 | 0.1532 | 5.37 | 0.000 | 6.148
X2 | 0.2465 | 0.1059 | 2.33 | 0.021 | 1.272
X3 | -0.01369 | 0.01677 | -0.82 | 0.415 | 1.361
X4 | 0.03747 | 0.02047 | 1.83 | 0.069 | 1.467
X5 | 0.002483 | 0.005663 | 0.44 | 0.662 | 4.684
X6 | 0.06053 | 0.01036 | 5.84 | 0.000 | 2.591
X7 | 0.003679 | 0.002776 | 1.33 | 0.187 | 1.925
X8 | -0.00049155 | 0.00007112 | -6.91 | 0.000 | 2.08
X9 | 0.1776 | 0.1305 | 1.36 | 0.176 | 1.068
Table 1: The regression coefficient table

## Slide 7
Case Example - Regression
The predictive model - Issues
- Multi- colinearity exists
- The R2 value is not very high
 | Y | X1 | X5
Y | 1 |  | 
X1 | 0.676 | 1 | 
X5 | 0.656 | 0.819 | 1
From the table 1, it can be observed from the values of VIF that the variables X1 and X5 are highly correlated.
The correlation coefficient between X1 and X5 and that between X1 and Y and X2 and Y are given in Table-2.
Table -2: Correlation coefficient among Y, X1 and X5.
Variable X1removed from the model and new model developed with the strength is measured by R2 = 0.636 and R2adj = 0.619.

## Slide 8
Case Example - Regression
Resolving Multi- colinearity issue
Two approaches
identify and remove one of the variables form a pair which are highly correlated.
Use Principal Component Regression (PCR)
Regression analysis based on PCA are not carried out because:
The principal components may have no sensible physical interpretation.
The principal components are linear combination of all the independent variables. Consequently, in an industrial setup exercising control over all the independent variables may turn out to be a formidable task if the regression model is built on the principal components.
The dependent variable may not be well predicted by the principal components, even if it is well predicted by some other linear combination of the independent variables.

## Slide 9
Case Example - Regression
The predictive model (Final) :
with R2 value of 0.72 and R2adj value of 0.70.
Fig-3: The predicted vs actual graph for MSFE efficiency

## Slide 10
Case Example - Regression
The Optimum values of X’s:
The optimum values of the parameters are found through MS-EXCEL solver
Cooling Tower Pressure ( X2 ) at 1.38 kg/cm2
Cooling Tower Temp ( X3 ) at 28 oC
A-1 temperature ( X5 ) at 87 oC
H-1 temperature ( X6 ) at 102 oC
DSH temperature ( X7 ) at 130oC
Steam flow (X8) at 4800 M3/hr.
The corresponding optimum steam efficiency has been found to be 3.48 M3 per ton of steam.

## Slide 11
Case Example - Regression
Implementation and Benefits
Variable | Status | N | Average | Stdev
MSFE Efficiency | Before | 51 | 3.2839 | 0.1392
 | After | 62 | 3.4830 | 0.1227
Table-3: Comparison of MSFE efficiency before and after implementation
This project has produced a direct saving to the tune of INR 12.5 lakhs for the company per annum